## Slide 1
To the truth of things,
With a focused purpose.
Optosky (Xiamen) Photonics Co., Ltd.
optosky.com
4008-508-928
Leading Enterprises in the Spectrometer Industry
Pioneering Global Innovation and Development in Raman Spectroscopy Technology
International Spectroscopy Experts / Over 20 Years of Experience
Products Exported to More Than 50 Countries
Application of GY1000 Moisture Meter in Tobacco

## Slide 2
CONTENTS
Summary
01
02
03
Introduction
GY1000 Introduction & Application in Tobacco

## Slide 3
CONTENTS
Summary
01
02
03
Introduction
GY1000 Introduction & Application in Tobacco

## Slide 4
Introduction
Modern cigarette production involves seven key manufacturing processes: primary tobacco curing, threshing and redrying, tobacco fermentation, cigarette blending, cigarette primary processing, cigarette rod forming, and cigarette packaging.
Warehouse
Cigarette Packaging
Cigarette Rod Making
Cigarette Primary Processing
Cigarette Blending
Tobacco Fermentation
Threshing & Redrying
Primary Tobacco Curing
Notes: 卡尔费休水分仪

## Slide 5
Introduction
Process Moisture content | 
Primary Tobacco Curing | Reduces fresh tobacco leaf moisture from 80%-90% to wilted and dried state
Threshing and Redrying | Controls tobacco moisture content to 11%-13%
Tobacco Fermentation | Customizable moisture detection to prevent deterioration
Cut Tobacco Processing | Maintains tobacco moisture content at 11%-13%
Primary Tobacco Curing
Reduces leaf moisture from 80%-90% to complete dryness.
Threshing and Redrying
Adjusts moisture to 11%-13% to prevent mold.
Tobacco Fermentation
Natural or artificial methods enhance leaf color, aroma, and flavor.
Cigarette Blending
Combines different tobacco types and flavorings.
Cigarette Primary Processing
Produces cut tobacco with moisture content of 11.5%-14.0%.
Cigarette Forming
Uses specialized machinery to produce standardized cigarettes from qualified materials.
Cigarette Packaging
Protects product quality while ensuring easy identification, transport and sales.
Process Stages Requiring Moisture Content Monitoring

## Slide 6
Model Selection and Training
Introduces the fundamental principles and characteristics of common AI models such as Support Vector Machines, Neural Networks, and Deep Learning, analyzing their applicability in tobacco leaf spectral monitoring.
Common AI Models
Employs methods like cross-validation to train AI models, reasonably divides training and test sets, optimizes model parameters, and enhances the model's generalization capability and recognition accuracy.
Model Training Methods
Utilizes metrics such as accuracy, recall, and F1 score to evaluate trained AI models, analyzes model performance strengths and weaknesses, and provides a basis for model selection and optimization.
Model Evaluation Metrics
Tobacco Leaf AI Algorithm Development

## Slide 7
Model Refinement
Parameter Tuning
Based on model evaluation results, adjust AI model parameters such as learning rate and regularization terms to further enhance model performance and stability.
Transfer Learning
Utilize transfer learning techniques to adapt pre-trained models for new tobacco leaf spectral monitoring tasks, reducing training time and computational resource requirements while improving model adaptability.
Model Ensemble
Implement ensemble methods like Bagging and Boosting to combine multiple AI models, enhancing robustness and recognition accuracy while reducing overfitting risks.
01
02
03
AI Model Optimization

## Slide 8
Summary
01
02
03
Introduction
GY1000 Introduction & Application in Tobacco
CONTENTS

## Slide 9
Principle Introduction
Measurement Principle:
水的近红外吸收峰比较
Water exhibits strong absorption characteristics for infrared light at specific wavelengths (as shown in the figure below left). When materials are irradiated with infrared light at these specific wavelengths, the water contained in the materials absorbs part of the infrared energy. The higher the water content, the more energy is absorbed. Therefore, the moisture content of the material can be calculated by measuring the reduction in reflected light. Based on this principle, GY1000 was developed using the more widely applicable theory of diffuse reflection of water.
Transmittance
Wavelength Characteristics
Too low absorption rate
Ideal absorption for industry
Excessive absorption, limited range
Optimal for industrial use
Characteristic spectral lines of water absorption in the infrared band
Comparison of near-infrared absorption peaks of water

## Slide 10
GY1000 Product Introduction
Detection Probe |  | 
1 | Measurement Range | 0~70%H2O
2 | Light Source | Imported Halogen Tungsten Lamp ¦ Service Life ≥ 5,000 Hours
3 | Measurement Wavelength | 4 Wavelengths, 8 Beams
4 | Detector | Cooled Imported PbS Detector
5 | Measurement Accuracy | < 0.3%
6 | Repeatability | < 0.1%
7 | Testing Speed | 25ms
8 | Measurement Distance | 250mm±100mm
9 | Spot Size | 50mm
10 | Protection Rating | IP65
Display (Optional) |  | 
1 | Touchscreen | 10-inch capacitive touchscreen
2 | Operating System | Windows 10
3 | Memory | 4GB RAM, expandable
4 | Probe Cable | Shielded twisted pair, customizable
5 | External Interfaces | DC power socket, Ethernet port, 2× USB
6 | Combination Method | Supports multi-probe connection

## Slide 11
GY1000 Tobacco Leaf Measurement
Sample Name | Oven-Drying Moisture Content | Instrument Measured Moisture Content
Tobacco Leaf | 9.10% | 8.56%
Tray Weight
Tobacco Leaf
Weight After Drying
Instrument Reading
Moisture Content

## Slide 12
GY1000 Tobacco Stem Measurement
Sample Name | Oven-Drying Moisture Content | Instrument Measured Moisture Content
Tobacco Stem | 20.99% | 20.44%
Tobacco Stem
Tray Weight
Weight After Drying
Instrument Reading
Moisture Content

## Slide 13
Summary
01
02
03
Introduction
GY1000 Introduction & Application in Tobacco
CONTENTS

## Slide 14
Summary
Rapid analysis：Near-infrared spectroscopy can complete moisture measurement of large quantities of tobacco samples in a short time，significantly improving detection efficiency.
Pollution-free：This technology requires no chemical reagents，completely avoiding environmental contamination.
Non-destructive：No sample preparation needed，enabling non-destructive analysis while preserving the original quality of tobacco leaves.
Online monitoring：Enables real-time online monitoring，facilitating immediate tracking of moisture changes in tobacco leaves.